## Slide 1: Etching Process Analysis through OES Spectrum Signal
BDA Eason Chiang

## Slide 2: Agenda
Recap OES analysis issues on Etching Process
  Use Random Forest Classifier to identify OES key wavelengths for defect defense.
  Moreover, we want to take the effect of each recipe to predict the intensity of OES signal

## Slide 3: Sketch of Plasma Etching & OES signal variation
Wafer
OES
sensor
Plasma Etching
Plasma
Wafer
Feed Gas
Tool Chamber Room
OES Signal
Etching
Recipe#A
Clean
Recipe#1
Wafer
Etching
Recipe#A
Wafer
…
Time
Byproduct Falling Down
(Plasma) Etching process carves wafer surface, and produces byproducts in the chamber room.
Chemical changes in chamber room reflects in OES signal.
OES: Optical Emission Spectroscopy
…
Time Seq. | Recipe | Cate.
1 | #A | Etching
2 | #1 | Clean
3 | #B | Etching
4 | #2 | Clean
… | … | …
3000 | #A | Etching
Byproduct falling down to center of wafer.
C
C
C
C
C
C
C
…
C
…
C
…

## Slide 4: Use Random Forest to identify OES key wavelength in particular recipe mix-run

## Slide 5: 逮到 830 的圖

## Slide 6: 換到其它 Mix-run 就不正確
兩張 OES 的比較圖
當多混了其它 Recipe
Mix-run 3 diff. recipes
當清潔的頻率不同
Clean more frequently

## Slide 7: Take Equivalent (當量) of recipe into account
Wafer
OES
sensor
Plasma Etching
Plasma
Feed Gas
Equivalent (當量) is one estimation value for the effect of etching and clean recipe. The estimated basis is “indestructibility of matter” theory (物質不滅).
Accumulate all the equivalents of recipes by time, we found that defect happened when Carbon is greater than Silicon, and the ratio comes to about 2.2+ times.
Time Seq. | Recipe | Cate. | C- Equiv. | Si-Equiv.
1 | #A | Etching | +200 | +100
2 | #1 | Clean | -100 | -50
3 | #B | Etching | +100 | +300
4 | #2 | Clean | -200 | -300
… | … | … | … | …
3000 | #A | Etching | +200 | +100
Byproduct falling down to center of wafer.
Defect Happened
No Defect Happened

## Slide 8: Apply Equivalent for prediction
Is it workable for F( features(當量) )= features(OES)?
It means that we can predict defect happen if we can predict OES signal jumping at some level.
Suggestions needed:
  How to get feature for F( features(當量) )? 
  How to get feature for features(OES)?  TSFRESH is ok?
Area of Signal
830 的圖
F( features(當量) )
features(OES)
那兩張累積圖
prediction
Total
L2L
F( )
W2W
Exponential Decay
…
Area of OES Signal

## Slide 9: 時間指數遞減做法 & L2L & W2W

## Slide 10: 結果頁

## Slide 11: TSFRESH
Time Series FeatuRe Extraction based on Scalable Hypothesis tests
The area of time series is one kind of features.
Feature Generation
Feature Extraction

## Slide 12: Feature significance test
Based on nonparametric hypothesis tests, do not make any assumptions about the distribution of the variables, which ensures robustness of the procedure.
Fisher’s Exact test: both the target and feature are binary
Kolmogorov-Smirnov test (binary feature):
Kolmogorov-Smirnov test (binary target):
Kendal rank test:
 | Target – Binary | Target – Non-Binary
Feature – Binary | Fisher’s Exact test | Kolmogorov-Smirnov test (Binary Feature/ Continuous Feature)
Feature – Non-Binary | Kolmogorov-Smirnov test (Binary Target) | Kendal rank test

## Slide 13: Benjamini-Yekutieli Procedure
nφ is the number of all null hypotheses and
q is the FDR level the procedure controls.
It will reject all hypotheses belonging to p-values that have a lower value than the p-value at the intersection, see the left side of Fig. 2(b).
Notes: http://www.unc.edu/courses/2007spring/biol/145/001/docs/lectures/Nov12.html

## Slide 14: Backup

## Slide 15: Diff. wavelength means diff. chemical element
Bromine
SF6
Chlorine

## Slide 16
Wafer
OES
sensor
Plasma Etching
Plasma
Wafer
Feed Gas
Chamber Room
OES Signal
Etching
Recipe A